Safe interventions - Aide memoire on machinery safety

# Hazard elimination and risk reduction

| Has the employer taken all reasonably practicable steps to eliminate/minimise the need for people to gain access into danger zones by: | Machine 1 | Machine 2 |
| --- | --- | --- |
|  | Y | N | NA | Y | N | NA |
| Minimising the chance of blockages (e.g. pre-sorting of feed materials, ensuring feed conveyors are evenly loaded, ensuring steady feed rates etc)? |  |  |  |  |  |  |
| Providing feed conveyors with reversing facility? |  |  |  |  |  |  |
| Ensuring machines and guards allow rodding of blockages from outside the guard enclosure? |  |  |  |  |  |  |
| Providing misfeed detection and warning systems? |  |  |  |  |  |  |
| Providing machinery that can be adjusted automatically (by motorised adjusters etc)? |  |  |  |  |  |  |
| Providing machinery that can be adjusted manually from outside the guard enclosure? |  |  |  |  |  |  |
| Ensuring dimensions in fixed guards for insertion of adjustment tools do not allow bodily access into the danger zone? |  |  |  |  |  |  |
| Providing viewing aids (e.g. internal lighting, clear viewing panels, CCTV, mirrors etc) that allow people to see critical parts of the process without the need to gain access? |  |  |  |  |  |  |

# Hardware

Machinery safeguarding, interlocks and emergency stop devices

Note – The quality of safeguarding and any associated interlocking devices will vary depending on the potential harm if access is gained behind it. Points to consider: How large is the opening when the protection is removed? Severity of injury? Frequency and/or exposure time to the hazard? Possibility of avoiding the hazard?

| Question | Machine 1 | Machine 2 |
| --- | --- | --- |
|  | Y | N | NA | Y | N | NA |
| Are you satisfied with the method of safeguarding? |  |  |  |  |  |  |
| Are you satisfied with the standard of safeguarding? |  |  |  |  |  |  |
| Are you satisfied that interlocking is provided where required? |  |  |  |  |  |  |
| Are you satisfied with the standard of interlocking where provided |  |  |  |  |  |  |
| Are all items of machinery fitted with one or more emergency stop devices (ESDs) that have clearly identifiable, visible and quickly accessible controls? |  |  |  |  |  |  |
| Where several machines operate together, does each ESD stop the other machines where necessary? |  |  |  |  |  |  |
| Do the ESDs stop the dangerous movement or process as quickly as possible without creating additional hazards? |  |  |  |  |  |  |
| Where necessary do the ESDs trigger safeguard movements e.g. release of clamping pressure? |  |  |  |  |  |  |
| Does the operation of the ESD require physical resetting to start the machine? |  |  |  |  |  |  |

Isolation and lock-off devices

| Where access is required, has the employer provided robust isolation and lock-off devices that ensure that: | Machine 1 | Machine 2 |
| --- | --- | --- |
|  | Y | N | NA | Y | N | NA |
| The drive to the dangerous part of the machine can be isolated from energy sources? |  |  |  |  |  |  |
| Any stored energy can be dissipated before access is allowed? |  |  |  |  |  |  |
| Actuators for energy isolation systems are suitably positioned, clearly labelled to identify the items of machinery they isolate and marked ON/OFF? |  |  |  |  |  |  |
| They are fitted with the means of locking in the off position where necessary? |  |  |  |  |  |  |

Procedures

Safe systems of work

| Where the need for access into danger zones cannot be eliminated, has the employer: | Machine 1 | Machine 2 |
| --- | --- | --- |
|  | Y | N | NA | Y | N | NA |
| Identified the tasks that require access?; |  |  |  |  |  |  |
| Performed a suitable and sufficient risk assessment for each task?; |  |  |  |  |  |  |
| Taken account of the potential for human error (e.g. slips or lapses of memory, communication errors etc) as part of the risk assessment?; |  |  |  |  |  |  |
| Taken account of the potential for violation of rules by employees and the factors that influence the potential for rule violation (e.g. workload, time pressures, practicality of the rules)?; |  |  |  |  |  |  |
| Taken account of the need for safe access and egress?; |  |  |  |  |  |  |
| Taken account of the risk of slips, trips and falls from height?; |  |  |  |  |  |  |
| Taken account of the risks from manual handling associated with the task?; |  |  |  |  |  |  |
| Taken account of the relevant instructions in machine manufacturers’ instruction manuals?; |  |  |  |  |  |  |
| Provided and maintained a suitable permit–to-work system where appropriate?; |  |  |  |  |  |  |
| Provided appropriate emergency shutdown procedures?; |  |  |  |  |  |  |
| Provided a safe system of work for each task?; |  |  |  |  |  |  |

Energy isolation and lock-off

| Are there robust energy and isolation lock-off procedures that: | Machine 1 | Machine 2 |
| --- | --- | --- |
|  | Y | N | NA | Y | N | NA |
| Specify the correct isolators for the intervention task?; |  |  |  |  |  |  |
| Check that stored energy has been dissipated where appropriate?; |  |  |  |  |  |  |
| Ensure the isolator(s) are securely locked in the off position?; |  |  |  |  |  |  |
| Include a final check to confirm that machinery has been isolated from all sources of energy? |  |  |  |  |  |  |
| Communicate the fact that people are working in the danger zone to everyone who needs to know e.g. anyone who might start the machine? |  |  |  |  |  |  |
| Personal padlocks are provided and, where appropriate, multiple lock hasps? |  |  |  |  |  |  |
| Spare keys for isolator locks are not accessible? |  |  |  |  |  |  |

Routine maintenance and inspection of safety related parts

Note – Please consider preventive maintenance and inspection by both the operator and maintenance staff. e.g. In many industries two levels of safety checks are appropriate: Daily visual and fictional tests; and Less frequent but more detailed inspections and checks carried out by a competent machine setter or maintenance staff.

| Has the employer provided effective procedures for routine maintenance, inspection/testing of and reporting defective: | Answer |
| --- | --- |
|  | Y | N |
| Fixed and moveable guards and access doors, gates, panels and electro-sensitive protective devices?; |  |  |
| Interlocking devices?; |  |  |
| Emergency stop devices (ESDs)?; |  |  |
| Power isolation devices? |  |  |

# Management system

Managing and organising the safe systems of work (SSOW)

| Is there evidence to show the following: | Answer |
| --- | --- |
|  | Y | N |
| Managers and supervisors understand and accept their responsibilities for the operation of the SSOW?; |  |  |
| Managers and supervisors are held accountable for the correct operation of the SSOW?; |  |  |
| That, where appropriate, employees or their representatives were adequately involved and consulted during the preparation of any safe systems of work they are required to follow?; |  |  |
| Rules relating to the SSOW are effectively communicated and understood?; |  |  |
| Employees required to apply and follow the SSOW have been properly trained in the SSOW?; |  |  |
| The SSOW are properly followed in practice?; |  |  |
| Managers and/or supervisors monitor compliance with the SSOW?; |  |  |
| Managers and/or supervisors take appropriate remedial action if SSOW are not followed properly?; |  |  |
| Managers review the operation of the SSOW at appropriate intervals? |  |  |

## Enforcement

| What was the highest level of enforcement action taken as a result of your visit? Tick boxes that apply. |  | Haz elim’n & risk reduct’n | Hardware | Procedures | Mgm’t system |
| --- | --- | --- | --- | --- | --- |
|  | Prosecution |  |  |  |  |
|  | PN |  |  |  |  |
|  | IN |  |  |  |  |
|  | Written |  |  |  |  |
|  | Verbal |  |  |  |  |